## Slide 1: STEEL DEFECT DETECTION
Deep Neural Networks and Applications with Tensorflow
City College of New York
Prof. Michael Grossberg
Team Members
Carlos Tavarez
Deepak Kumar
Divya Sankar
Sonali Shintre

## Slide 2: OBJECTIVE
The goal of this project is to classify and detect defects on steel sheets based on image input.
We breakdown our project into 3 components:
  Identify whether an input image has a defect
    This is a binary classification problem
  Identify the number of types of defects an image contains
    Multi-class classification problem, where each image can have up to 4 types of defects corresponding to classes [1,2,3,4]
  For each defect type, identify regions of the image that has this defect
    This is a image segmentation problem, where each pixel is labeled as having no defect or a defect of a particular type

## Slide 3: DATASET
The dataset is of size ~2GB and consists of 18076 images.
  There are 12568 images in the train set.
  There are 5506 images in the test set.
Of the training 12568 images, only 7095 images have defects, rest have no defects.
Each image is of size 1600*256
The location of the defects we given as encoded pixels. We have to decode them using a mask function to get the defect location.
Link to dataset - https://www.kaggle.com/c/severstal-steel-defect-detection/data

## Slide 4: Exploratory Data Analysis (EDA)
5473 images with no defects
7095 images have defects
Formed the dataset with labels 0 and 1 denoting no defects and defects respectively.
Inference – The number of images with and without defects are proportionate and the data seems quite balanced.

## Slide 5: Exploratory Data Analysis (EDA)
There are 4 categories of defects – Type 1 , Type 2, Type 3, Type 4.
Lot of images with defects belong to Type 3 defect.
Most of images with defects contain the defects of only one type;
In rare cases an image contains more than one defect
Inference
  The dataset is very imbalanced.
  Data augmentation has to be performed before training.
  Used resampling techniques for data augmentation

## Slide 6: Segmentation
Type 1 defects
Type 2 defects
Type 3 defects
Type 4 defects

## Slide 7: Binary Classification
Using CNN to classify images with and without defects
Resized images into (256,256,3)
4 convolutional layers, 4 maxpool and 1 Dense layer.
Used binary cross entropy for loss

## Slide 8: Binary Classification - Results
The model works quite well with training accuracy of 92% and testing accuracy of 87% with 15 epochs
The model generalizes well
The validation accuracy increases till 10 epochs after which it drops.
The loss keeps decreasing with the increase in number of epochs

## Slide 9: Binary Classification - Results
 | True No-Defect | True Defect
Predicted No-Defect | 1039 | 142
Predicted Defect | 181 | 1152
 | Precision | Recall
No-Defect | 0.85 | 0.88
Defect | 0.89 | 0.86
Precision-Recall Matrix
Confusion Matrix

## Slide 10: Multi Class Classification – Unbalanced classes
CNN model with 10 layers with 4 Conv2D, 4 maxpool and 2 Dense layers
Trained the model for 11 epochs – 50steps for each epoch
Got 76% accuracy for training and 78% for testing
The model was predicting only defect type 3
0 | 0 | 62 | 0
0 | 0 | 19 | 0
0 | 0 | 433 | 0
0 | 0 | 42 | 0
Predicted
Table 2. Confusion Matrix for training set.
0 | 0 | 630 | 0
0 | 0 | 157 | 0
0 | 0 | 3850 | 0
0 | 0 | 422 | 0
Predicted
True
Table 1. Confusion Matrix for training set.
True

## Slide 11: Multi Class Classification – balanced classes
After using the balanced data generator started generalizing and looking for differences between classes.
Data augmentation by fliping and rotating the image.
The model gave 47% accuracy for training and testing images.
Despite the training improved using balanced image generator we had low accuracy.
Source: https://medium.com/analytics-vidhya/how-to-apply-data-augmentation-to-deal-with-unbalanced-datasets-in-20-lines-of-code-ada8521320c9
36 | 5 | 5 | 16
0 | 19 | 0 | 0
88 | 51 | 173 | 121
3 | 1 | 1 | 37
Predicted
True
Confusion matrix

## Slide 12: Multi Class Classification – Fine tuning model
Train Accuracy: 0.55
Validation Accuracy: 0.55
45 | 4 | 7 | 6
1 | 18 | 0 | 0
115 | 38 | 212 | 68
5 | 1 | 4 | 32
Predicted
True
Train Accuracy: 0.55
Validation Accuracy: 0.51
46 | 1 | 8 | 7
1 | 18 | 0 | 0
74 | 15 | 249 | 95
5 | 0 | 3 | 34
Predicted
True
Train Accuracy: 0.7
Validation Accuracy: 0.66
33 | 3 | 14 | 12
0 | 19 | 0 | 0
22 | 18 | 283 | 110
1 | 0 | 8 | 33
Predicted
True

## Slide 13: Multi Class Classification – Final Model

## Slide 14: Defect Detection Through Image Segmentation
We perform defect detection using image segmentation i.e., label every pixel of the input as no defect or defect of a specific type
To perform image segmentation, we use the U-net architecture (first proposed for medical imaging)
  A popular architecture in a cla\ss of DNNs called Fully-Convolutional Nets (FCNs)
FCNs or U-net comprises of 2 parts:
  The first part is similar to image classification CNNs, that have a sequence of CONV/ReLU/MaxPool layers
  In the second part, instead of classification layers, transpose convolution is performed to gradually upsize the features and get the final segment map for each class
    Transpose convolution also uses feature from the first part of the model
  This gives the U-shape to the architecture
U-net architecture
Model adapted from:

## Slide 15: Model Architecture - Specifics
The input image is a 256*1600 image with 3 channels.
The model has 33 layers
  23 Conv2D layers
  5 Maxpool layers
  5 Conv2DTranspose layers
The total number of trainable parameters is 600,612.
The output is segment maps of the image for each defect class type.
256x1600
128x800
64x400
32x200
16x100
8 channels
16 channels
32 channels
64 channels
128 channels
4 channels
One for each defect type
3 channels

## Slide 16: Defect Detection - Results
Inference
Due to the imbalance in data the model predicts the defects as type 3.
Used subset of the data with more balanced images in each class and trained the u-net model. Gave better results but again the model was biased towards the defect class with more number of images.
Original image
Segment map- type 1
Segment map- type 2
Segment map- type 3
Segment map- type 4
Final Output
Output Images
No defect
Defect Images
Chart: 
| 1 | 2 | 3 | 4 | 5
Training loss | 1.0293 | 0.898 | 0.807 | 0.7486 | 0.7028
Validation loss | 0.9248 | 0.9112 | 0.8625 | 0.8165 | 0.8419
Training vs. Validation Loss
Epochs
Loss

## Slide 17: Contributions
Sonali – EDA and data augmentation and compiled the project report.
Deepak – Binary Classification using CNNs.
Carlos – Multi-Class classification and balancing the data.
Divya – Defect Detection through segmentation and managing the github repo.
The team members met 2-3 times every week for about an hour and discussed the issues and further steps.
We were in constant communication with each other through blackboard and helped each other
Carlos
Divya
Deepak
Sonali
Commits as of 05/14
Divya
Carlos
Deepak
Sonali
Total no. of commits in the repo

## Slide 18
THANK YOU!